## Slide 1: MPEG-4 Audio
Schuyler Quackenbush
AT&T Laboratories
Florham Park, NJ 07932 USA
srq@research.att.com

## Slide 2: Outline
Overview
Audio coding tools
Audio profiles
Applications
Summary

## Slide 3: What is MPEG-4?
MPEG-2
  bit stream and decoder
MPEG-4
  multiple audio objects and associated operations
  1 input stream per object
  1 output stream per terminal

## Slide 4: Media Objects
Objects
  Natural audio
  Synthetic audio
  Control
Operations on objects
  Synchronize
  Decode
  Compose into compound objects
  Present
  Interact

## Slide 5: Advantages of Object Framework
Each signal coded with most efficient coding system
  Natural
  Synthetic
Composition of objects into audio scene
  Rate conversion
  Mix and Equalization
  Effects
Final mix is done in the terminal

## Slide 6: Audio Object Functionalities
Signal compression
Scalability
  bit rate
  signal bandwidth
  presentation rate
  encoder or decoder complexity
Extraction and re-use
Robustness to channel errors

## Slide 7: Scalability

## Slide 8: Audio Decoder Structure

## Slide 9: Audio Tools
Speech coding
General audio coding
Scalable coding
Synthetic audio coding
Audio composition

## Slide 10: The Speech Coding Advantage
Excellent compression by using source model
  Linear Predictive Coding (LPC)
  Pitch or noise excitation
Better compression than “general audio” coders
  only for “clean speech” from single talker

## Slide 11: MPEG-4 Speech Coders
Harmonic Vector Excitation Coder (HVXC)
Code Excitation Linear Prediction (CELP)
Wideband CELP

## Slide 12: Demonstration
1.7 kb/s variable rate HVXC
12 kb/s CELP
24 kb/s Wideband CELP

## Slide 13: General Audio Coding
Does not assume any source model
  therefore works on any audio signal
Exploits model of human hearing
  common to all listeners
  simultaneous masking model
Advanced Audio Coding
  in MPEG-2 and MPEG-4

## Slide 14: Audio Coding Gain
Statistical signal redundancy
  high-resolution filterbank
Perceptual signal irrelevancy
  model of human auditory masking
Variable length quantizer
Demonstration
  AAC 96kb/s stereo

## Slide 15: Scalable Coding
Base plus one or more enhancement layers

## Slide 16: Structured Audio Coding Tools
Virtual Instrument synthesis language
  Structured Audio Orchestra Language (SAOL)
  Create and manipulate virtual instruments
Wavetable synthesis
  Structured Audio Sample Bank Format (SASBF)
Control language
  Structured Audio Score Language (SASL)
TTS Interface

## Slide 17: Audio Composition
Controls sound presentation
  mix audio objects
  render, spacialize
AudioBIFS
  specifies composition
    uses SA tools
  permits user interaction
    environment-aware spacialization

## Slide 18: Structured Audio Demonstration
Natural audio, synthetic audio and audio composition
Not all tools run at the same time
    TTS 50 b/s
    Parametric Coder 2 kb/s
    Speech Coder 16 kb/s
    Structure Audio 1 kb/s
    Audio Composition 50 b/s
    Total rate 16 kb/s

## Slide 19: Audio Coding Performance
Broadcast quality at
  320 kbit/s for 5 channels
  128 kbit/s for stereo
AAC at 96 kb/s stereo is as good as
  AC-3 at 160 kbit/s (66% better)
  Layer II at 192 kbit/s (100% better)
  Layer III at 128 kbit/s (33% better)

## Slide 20: Speech Coding Performance
Comparable quality at 8 kHz sampling rate
  MPEG-4 CELP at 6 kb/s
  G 723.1 at 6.3 kb/s
Comparable quality at 16 kHz sampling rate
  MPEG-4 CELP at 24 kb/s
  G.722 at 56 kb/s (estimated)

## Slide 21: Scalable Coding Performance
Scalable coders are
  more flexible than fixed rate coders
  require ~15% more rate than fixed rate coders

## Slide 22: MPEG-4 Patent Licensing Status
MPEG-4 Industry Forum
  www.m4if.org
Have identified first phase of essential patents
Audio Licensing Committee will license
  Speech profile
  Mobile Audio Internetworking profile
  High Quality Audio profile

## Slide 23: Application: Internet Streaming Audio
64 kb/s stereo Entertainment Quality
96 kb/s stereo Very Good
128 kb/s stereo Broadcast Quality

## Slide 24: Scalable Simulcast

## Slide 25: Summary
MPEG-4 provides enhanced functionality
  state of the art compression
  scalability (bitrate, bandwidth, complexity)
MPEG-4 is a Media-Object based standard
  multiple natural audio coders
    each optimized for a class of signal
  structured audio coding
    score driven algorithmic synthesis
  audio composition
    user interaction

## Slide 26: Future of MPEG-4
Not just compression
Content representation
  Content will be composed in MPEG-4
  Content author can control
    presentation of audio scene
    user interaction with audio scene
Will be the most pervasive standard for complex multi-media presentations